## Slide 1: PI-STORAGE: A COST-EFFECTIVE AND SECURE RASPBERRY PI-BASED NAS SOLUTION
Bangalore Institute of Technology
K.R. Road, V V Puram, Bangalore-560004
Department of Electronics and Communication Engineering
MAJOR-PROJECT-22EC76 PRESENTATION
Likhitha K
Assistant Professor
Dept. of ECE
BIT.
Under the guidance of:
Abhishek Agarwal 1BI22EC003
Aditya S Gowda 1BI22EC007
Aditya Umesh 1BI22EC008
Amruth Shirin K H 1BI22EC012
Presented by

## Slide 2
Bangalore Institute of Technology
Dept. of ECE, BIT
CONTENTS
CONTENTS
INTRODUCTION
PROBLEM STATEMENT
LITERATURE SURVEY
METHODOLOGY
CONCLUSION
REFERENCES

## Slide 3
Bangalore Institute of Technology
Dept. of ECE, BIT
INTRODUCTION
Pi-Storage is a cost-effective, secure, and energy-efficient Network Attached Storage (NAS) solution built using a Raspberry Pi. Designed for personal users and small businesses, it offers centralized file storage and management over LAN and the internet. By leveraging open-source tools and standard protocols, Pi-Storage ensures flexibility, scalability, and platform compatibility.
Key Benefits:
Low Power Usage – Ideal for 24/7 operation
Affordable – Much cheaper than commercial NAS systems
Secure – SSH, VPN, TLS/SSL, and firewall integration
Redundant Storage – RAID support using mdadm
Cloud Sync – Real-time backup via Next cloud/OwnCloud
Cross-Platform Access – Works on Windows, Linux, macOS
Modular Expansion – Supports Docker, Plex, Jellyfin

## Slide 4
Bangalore Institute of Technology
Dept. of ECE, BIT
PROBLEM STATEMENT
Problem Statement: High-cost, power-intensive NAS solutions are inaccessible to individuals and small businesses. There is a need for a secure, energy-efficient, and affordable storage system that offers remote and local access.
Scope:
Build a low-cost NAS using Raspberry Pi
Support SMB, NFS, SFTP for cross-platform file sharing
Enable RAID via mdadm for redundancy
Add cloud sync (Nextcloud/OwnCloud), media streaming (Plex/Jellyfin)
Include web-based management (OpenMediaVault)
3. Limitations:
Limited performance due to Raspberry Pi hardware
Not suitable for enterprise-scale storage or high concurrency
Software RAID only (no hardware RAID support)
Requires technical setup for VPN and remote access
Limited number of external drives supported

## Slide 5
Bangalore Institute of Technology
Dept. of ECE, BIT
LITERATURE SURVEY
SL.NO | TITLE | AUTHORS | YEAR | DESCRIPTION
1 | DIY Raspberry Pi NAS | Smith et al. | 2020 | Provided the basic hardware setup and architecture for building a NAS using Raspberry Pi.
2 | Low-Cost NAS using RPi | A. Kumar et al. | 2021 | Informed the selection of cost-effective components and power-efficient design choices.
3 | Software RAID with mdadm on Linux | K. Raj et al. | 2021 | Guided the implementation of RAID 1 using mdadm for redundancy and data protection.
4 | Cloud Sync with OwnCloud on RPi | Jane Doe et al. | 2022 | Guided the implementation of RAID 1 using mdadm for redundancy and data protection.
5 | OpenMediaVault Performance on RPi | L. Zhang et al. | 2023 | Evaluated OpenMediaVault performance to select an optimal NAS management platform.

## Slide 6
Bangalore Institute of Technology
Dept. of ECE, BIT
CIRCUIT DIAGRAM
BLOCK DIAGRAM:

## Slide 7
Bangalore Institute of Technology
Dept. of ECE, BIT
METHODOLOGY
1.Hardware Setup:
Connect Raspberry Pi 4/5 with external HDD/SSD via SATA-to-USB adapter.
Ensure proper power supply for external drives.
2.Operating System Installation:
Install Raspberry Pi OS (Lite/Desktop) or Debian-based OS.
Update packages and configure SSH for remote access.
3.File Sharing Configuration:
Install and configure Samba (SMB), NFS, and SFTP for LAN access.
Set up user permissions and shared directories.
4.RAID Configuration:
Use mdadm to set up software RAID (e.g., RAID 1 for redundancy).
5.Cloud Sync Integration:
Deploy Nextcloud or OwnCloud for real-time backup & remote access.
6.Security Implementation:
Enable SSH, TLS/SSL encryption, and VPN (WireGuard/OpenVPN).
Set up firewall rules using UFW/IPTables.
7.Web Interface & Expansion:
Install OpenMediaVault for browser-based management.
Use Docker for deploying Plex/Jellyfin and other services.

## Slide 8
Bangalore Institute of Technology
Dept. of ECE, BIT
HARDWARE AND SOFTWARE REQUIREMENTS
HARDWARE | SOFTWARE REQUIREMENTS
Raspberry Pi 4 / 5: Compact and energy-efficient computing platform. External HDD/SDD: Storage media for NAS functionality. SATA-to-USB 3.0 Adapter: Connects storage device to Raspberry Pi. MicroSD Card (32GB or higher):For OS installation and boot. Power Supply (3A USB-C): Required to power Raspberry Pi and peripherals. Ethernet Cable / Wi-Fi Adapter: Network connectivity (LAN/Internet). | OS: Raspberry Pi OS / Debian Linux. NAS Management: OpenMediaVault. File Sharing: Samba (SMB), NFS, SFTP, FTP. Storage Tools: mdadm, rsync, cron. Cloud Sync: Nextcloud, OwnCloud. Security: WireGuard, OpenVPN, UFW, IPTables. Expansion & Media: Docker, Plex, Jellyfin.

## Slide 9
Bangalore Institute of Technology
Dept. of ECE, BIT
CONCLUSION
The Pi-Storage project successfully demonstrates a cost-effective and secure NAS solution using Raspberry Pi. It provides centralized storage with cross-platform file sharing, RAID-based redundancy, remote access via VPN, and cloud synchronization using open-source tools. With features like web-based administration and media streaming, it is well-suited for individuals, small businesses, and educational environments seeking an energy-efficient and scalable storage system.
Limitations & Future Work
Raspberry Pi hardware limits performance, making it less suitable for high-concurrency or enterprise-scale use.
Only software-based RAID is supported future versions could explore hardware RAID or clustering for better reliability.
Requires manual setup and technical knowledge, a simplified web/mobile interface could improve usability.
Limited number of external drives; scalability could be enhanced using Raspberry Pi clustering or SATA expansions.
Security depends on proper configuration future work may include blockchain integration and automated security monitoring.

## Slide 10
Bangalore Institute of Technology
Dept. of ECE, BIT
REFERENCES
[1] Smith et al., “DIY Raspberry Pi NAS,” 2020.
[2] A. Kumar et al., “Low-Cost NAS using RPi,” 2021.
[3] K. Raj et al., “Software RAID with mdadm on Linux,” 2023.
[4] Jane Doe et al., “Cloud Sync with OwnCloud on RPi,” 2022.
[5] L. Zhang et al., “OpenMediaVault Performance on RPi,” 2021.